## Slide 1: Multi-Facet Approach to Reduce Energy Consumption in Clouds and Grids: The GREEN-NET Framework
Georges da Costa2, Marcos Dias de Assunção1, Jean-Patrick Gelas1, Yiannis Georgiou3, Laurent Lefèvre1, Anne-Cécile Orgerie1, Jean-Marc Pierson2, Olivier Richard3, Amal Sayah2
1 INRIA RESO, ENS de Lyon
2 IRIT, Université Paul Sabatier, Toulouse
3 MESCAL, Laboratoire ID-MAG, Grenoble
Passau, Germany, April 2010

## Slide 2: Introduction
Challenge of managing and providing resources to user applications
  Server farms, Grids, data centres and Clouds
Grid’5000:
  Experimental Grid composed of 9 sites distributed across France
  OAR*: open-source Resource Management System (RMS) based on high-level components
  Job types:
    Advance reservations
    Best-effort
* Nicolas Capit et al., A Batch Scheduler with High Level Components, 5th IEEE International Symposium on Cluster Computing and the Grid (CCGrid'05), pp. 776-783, May 2005

## Slide 3: Introduction
Energy consumption of ICT
  CO2 footprint of Grids and Clouds
  Existing hardware and cooling solutions
  Improvements of the software stack
  Forums and actions
Users’ awareness of energy consumption
OMG! That’s a lot!

## Slide 4: The GREEN-NET Framework

## Slide 5: Outline
Informing the users
  Energy meters and interface library
  Presenting energy consumption data
Involving the users
  Power save mode of OAR
Autonomic energy aware support
  Exploring idle resources
  Predicting characteristics of advance reservations

## Slide 6: Energy Meters
Power meter HAMEG HM8115-2
  Used for calibrating other equipments
Omegawatt box
  6 or 48 ports, communication via serial port
  Deployed in three sites of Grid’5000 (162 nodes)
    Lyon, Toulouse and Grenoble
  One measurement per second
Heterogeneity of energy sensors

## Slide 7: Collecting and Exposing Information
Library for interfacing with energy sensors
Client-side applications to obtain and store the energy consumption data
Applications to create graphs that display the energy consumed by equipments
Users can check how much energy their applications consume

## Slide 8: Outline
Informing the users
  Energy meters and interface library
  Presenting energy consumption data
Involving the users
  Power save mode of OAR
Autonomic energy aware support
  Exploring idle resources
  Predicting characteristics of advance reservations

## Slide 9: The Power Save Mode of OAR
Power saving job type
  It allows users to control the performance and power consumption of computing nodes during their jobs’ execution
  CPU frequency scaling and hard-disk spin down
  Support for other device types in future
Trade-off between energy savings and performance degradation

## Slide 10: Experimental Scenario
Comparison among four cases:
  Normal execution, HDD spin-down, CPU Freq., and CPU freq. + HDD spin-down
9 nodes Intel Xeon dual-CPU 2.5GHz QuadCore with 8GB of RAM
NAS NPB benchmarks
MPI 3.3 implementation and 64 processes

## Slide 11: Experimental Results
Method | HDD Spin | CPU Freq. | HDD Spin + CPU Freq.
EP | 2.5 / 0 | 10.3 / -18.9 | 12.2 / -20.5
SP | 1.6 / 0.3 | 8.5 / -1.3 | 10.2 / -1.5
BT | 2 / -0.4 | 9 / -5.4 | 10.4 / -5.5
LU | 2.2 / 0.2 | 9.5 / -7.6 | 11.5 / -10.8
CG | 2 / -0.13 | 8.2 / -1.4 | 10 / -3.1
IS | 1.4 / 1.5 | 6.4 / -1.5 | 10 / -7.2
MG | 1.2 / -1.1 | 8.2 / -0.5 | 9.8 / -3.4
Overall | 1.8 / 0.05 | 8.5 / -5.2 | 10.5 / -7.4
Energy saving (%) / Performance gain (%)

## Slide 12: Outline
Informing the users
  Energy meters and interface library
  Presenting energy consumption data
Involving the users
  Power save mode of OAR
Autonomic energy aware support
  Exploring idle resources
  Predicting characteristics of advance reservations

## Slide 13: Exploring Idle Periods
Parameters:
  Node_manager_idle_time = 600 seconds
  Node_manager_sleep_time = 600 seconds
  Node_sleep_cmd = PowerOFF script
  Node_wakeup_cmd = PowerON script
Time
Current time
Time_last_res_finished
Time_last_res_starts
Idle_time
Sleep_time
Green management algorithm:
  Node sleep:
    IF Idle_time > Node_manager_idle_time AND Sleep_time > Node_manager_sleep_time THEN
      Exec Node_sleep_cmd
  Node wake up:
    IF sleeping node is needed THEN
      Exec Node_wakeup_cmd

## Slide 14: Experimental Scenario
Traces from DAS-2 clusters
  32 nodes
  Resource utilisations of 50.32% and 89.62%
  Durations of 7.25 and 7 hours
Management modes:
  Normal
  Green
Deployment of OAR on 33 nodes
  1 master node and 32 workers

## Slide 15: Energy Consumption: 50.32% resource utilisation

## Slide 16: Energy Consumption: 89.62% resource utilisation

## Slide 17: Experimental Results
Parameters | 1 | 2 | 3 | 4
Management mode | Normal | Green | Normal | Green
System utilisation (%) | 50.32 |  | 89.62 | 
Total number of jobs | 309 |  | 188 | 
Duration of traces (H) | 7.25 |  | 7 | 
Energy consumed (KWh) | 42.7 | 30.6 | 40.7 | 36.6
Average energy consumed (KW) | 5.9 | 4.2 | 5.8 | 5.2
Average job waiting time (seconds) | 8 | 829 | 1 | 218
Experiments

## Slide 18: Predicting the Next Reservation
Next reservation Re = (le, ne, te)
Method 1: At time t, the estimated start time of Re is the average of the arrival of reservations after time of the day t on:
  The two previous days
  The same weekday of the previous week
  i.e. te = 1/3 [tt,j-1 + tt,j-2 + tt,j-7] + t_feedback
Method 2: Average of characteristics of 5 previous reservations
Logs of advance reservation requests
Length or duration
Number of nodes
Start time

## Slide 19: GreenNet Policies
User: always obeys the user’s demands
Fully-green: uses the solution that saves the most energy
**%-green: handles ** of requests, taken at random, with the fully-green scheme and the rest with the user policy
Deadline: uses the fully-green approach if it does not delay the request for more than 24h of the start time required by the user

## Slide 20: Experimental Results
Replay of Grid’5000 logs

## Slide 21: Conclusions and Future Work
The GREEN-NET Framework
  Informing users, involving users, and autonomic energy-aware resource management
Power save mode of OAR
Switching off unused resources
  Predicting the characteristics of reservations
Analysis of energy consumption logs
Network equipments and protocols
Virtualisation technologies

## Slide 22: Thank you!
Questions & Answers