## Slide 1: The Green Grid’5000: Instrumenting and Using a Grid with Energy Sensors
Marcos Dias de Assunção, Jean-Patrick Gelas,
Laurent Lefèvre, Anne-Cécile Orgerie
INRIA RESO, Université de Lyon
École Normale Supérieure
46, allée d’Italie
69364 Lyon Cedex 07 - France
Poznań, Poland, May 2010

## Slide 2: Introduction
Challenge of managing and providing resources to user applications
  Server farms, Grids, data centres and Clouds
The Grid’5000:
  Experimental Grid composed of 9 sites distributed across France
  OAR*: open-source Resource Management System (RMS) based on high-level components
  Resource requests:
    Advance reservations
    Best-effort jobs
* Nicolas Capit et al., A Batch Scheduler with High Level Components, 5th IEEE International Symposium on Cluster Computing and the Grid (CCGrid'05), pp. 776-783, May 2005

## Slide 3: Introduction
Energy consumption of ICT
  CO2 footprint of Grids and Clouds
  Existing hardware, software and cooling solutions
Evaluation of proposed solutions
The energy sensor infrastructure:
  Users’ awareness of energy consumption
  Improving the design of user applications
  Energy-aware Grid middleware
  Power management policies
  Repository of energy consumption data

## Slide 4: The GREEN-NET Framework*
* G. Costa et al., Multi-Facet Approach to Reduce Energy Consumption in Clouds and Grids: The GREEN-NET Framework. In 1st Int. Conf. on Energy Efficient Computing and Networking, Passau, 2010.

## Slide 5: The Energy Sensors
Omegawatt box
  6 or 48 ports, communication via serial port
  Deployed in three sites of Grid’5000
  Lyon, Toulouse and Grenoble
Library for interfacing with energy sensors
Client-side applications to obtain and store the energy consumption data

## Slide 6: The Energy Consumption Information
Periodicity of energy measurements:
  Administrators’ requirements
  Performance and energy consumption of applications
  Grid middleware designers
  One measurement per second for each equipment
Data storage:
  Raw data (text files)
  Last values (text files in memory)
  Round-robin databases*
* RRD, http://oss.oetiker.ch/rrdtool

## Slide 7: Displaying the Energy Consumption Information

## Slide 8: Example I
Profiling the energy consumption of applications

## Slide 9: Example II
Improving the Grid middleware and policies
~14% of the electricity consumed by the platform during ~5 months

## Slide 10: Example III
Understanding the overall infrastructure

## Slide 11: Conclusions and Future Work
The GREEN-NET framework
Data requirements and management
Analysis of energy consumption logs
Future work
  Grid’5000 API
  Network equipments and protocols
  Virtualisation technologies
  Repository of energy consumption data

## Slide 12: Thank you!
Questions & Answers
Email: assuncao at acm.org